INDUSTRY NUMBERING COMMITTEE (INC)

CONTRIBUTION NPA-194

________________________________________________________

INC Subcommittee: NPA

________________________________________________________

Issue Number: 459

Contribution Title: Department of the Navy (DON) Request for NPA 366 to Overlay United States Portion of Country Code 1 Number Plan Areas (Geographic)

________________________________________________________

Source: U.S. Department of the Navy

________________________________________________________

Abstract:

Date: 12/9/04

________________________________________________________

NOTICE

This contribution has been prepared to assist the Industry Numbering Committee.  The contribution is offered to the committee as a basis for discussion and is not a binding proposal on the U.S. Navy, which reserves the right to amend or withdraw the statements contained herein at any time.

INC Issue Number: 459

Date: Tuesday, February 08, 2005

8:00 AM to Noon -  NPA Subcommittee Session

Subject:

Department of the Navy (DON) Request for NPA 366 to Overlay United States Portion of Country Code 1 Number Plan Areas (Geographic)

Related Previous INC Issues:

None

General Description

On October 11, 2004 the Department of the Navy submitted an Issue Statement to the INC for consideration. The Issue requested the DON be granted one (1) single NPA to manage and provide for its own use with its numerous services providers. This NPA would be for exclusive use of the DON and would be a geographic overlay NPA for the United States portion of the Country Code 1 Number Plan Areas. All current DON number assets provided by service providers within affected area would be returned to NANPA once converted to NPA 366.

On November 4, 2004 the Department of the Navy’s INC Issue was presented to the North American Numbering Council (NANC) which instructed the INC’s Chairman Ken Havens to review the request for technical feasibility and report back to the NANC as to whether the submission is technically feasible and does not cause technical problems for the existing telecommunications numbering plan. The INC is not to review the business case or policy components of this request. It was agreed that the NPA sub-committee was delegated responsibility of reviewing this requirement.

The DON Representative can find no technical concerns regarding implementing its request. It would be treated as the same as any typical NPA overlay plan, just adding the 366 NPA to all existing Number Plan Areas.

Implementation of Overlay Plan

Implementation of the overlay of the United States portion of Country Code 1 Number Plan Areas would be as follows:

|  | Time | Date |
| --- | --- | --- |
| Customer education period begins |  | TBD by NANPA |
| Start of 10-digit permissive dialing | 12:01 AM Eastern | TBD by NANPA |
| End of permissive dialing and start of mandatory 10-digit dialing | 12:01 AM Eastern | TBD by NANPA* |
| Earliest new NPA central office code activation date |  | TBD by NANPA |
| Earliest date central office codes in the new NPA may be ordered through NANPA |  | TBD by NANPA |

* NPA Effective Date

During the permissive dialing period, subscribers may dial local calls within the overlay area on either a 7-digit or 10-digit basis, but will be encouraged to dial 10-digits. After the permissive period ends, all calls must be dialed using 10-digits.

When preparing for overlay area code relief, carriers are strongly encouraged to prepare their switches to begin sending 10 digits prior to the mandatory 10-digit dialing conversion date for customers.

Dialing Plan

Coincident with the introduction of mandatory 10-digit dialing when NPA Effective Date by NANPA, the dialing plan for the 366 NPA and United States portion of the Country Code 1 Number Plan Area will be as follows:

| Type of call | Call terminating in | Dialing plan |
| --- | --- | --- |
| Local call | Home NPA (HNPA) or Foreign NPA (FNPA) | 10-digits (NPA-NXX-XXXX) |
| Toll call | HNPA or FNPA | 1 + 10-digits (1 + NPA-NXX-XXXX) |
| Operator Services | Credit card, collect, third party | HNPA or FNPA 0 + 10-digits (0 + NPA-NXX-XXXX) |

Network Testing

All international and domestic carriers should ensure that the new 366 NPA has been activated throughout their networks prior to date to be determined by NANPA. A test number to verify the routing to the new NPA will be in service beginning when required. The test number to verify the routing to the 366 NPA is 366-366-1111. A recorded announcement will indicate that the test call has been successfully completed.

General Information

The information in this planning letter reflects detailed information about NPA relief activities. The information has been derived from commission orders and from industry implementation decisions. The implementation of the plan described in this letter is the responsibility of individual service providers, and NANPA does not guarantee that the activities and plans will occur exactly as described herein.