## Slide 1: Telephone Numbers and IP Networks
Possible Impacts of IP Networks on Numbering
Tom McGarry, Neustar Fellow
6-10-14

## Slide 2: Addressing
Additional addressing information for IP
  In addition to CO code = switch & SP
  Could be IP address, URI, Tier 2 address, maybe other
  Could be at the SP level, CO code level or TN level
    TN level IP routing subject of SIP Forum/ATIS NNI group effort
Fewer POIs for IP
  Rather than 1/LATA, perhaps 2-10 for entire NANP
    Fewer POI addresses
    States w/o POIs
  NPA or NPA-NXX could be associated with multiple POIs
    Impact to NPAC?
  Phasing out of LATA tandems, replaced by direct connect or 3rd party transit provider

## Slide 3: Allocation
Allocation to non-TSPs, i.e., Vonage petition
Allocation not tied to a LATA and rate center
Allocation in blocks smaller than 1K
Non-geographic numbers

## Slide 4: Authentication
STIR required for IP transit
  Association of digital certificate with a TN to combat spoofing
  Rapidly becoming a hot button issue
STIR digital certificate administration
  Allocation
  Porting
  Addressing already allocated TNs

## Slide 5: Telephone identifiers
Telephone number – the number dialed to reach the user
Routing identifier – enables call routing and session establishment between, and sometimes, within networks
  Today VoIP uses LRNs
  LRNs are E.164 numbers
Subscription ID – identifies the user to networks
Equipment ID – assigned by equipment manufacturer and identifies the device to networks
IP address – assigned to a device for IP communications
Identifier | Wireline | 3GPP2 | 3GPP | VoIP
E.164 number | TN | MDN | MSISDN | TN
Routing identifier | LRN | LRN | LRN | URI
Subscription ID | NA | MIN (E.164) | IMSI (E.212) | UN/PW
Equipment ID | NA | ESN, MEID | IMEI | MAC
IP address | NA | DHCP | DHCP | DHCP

## Slide 6: Future of telephone numbers
No replacement for TNs likely
  No globally administered resource for identifying users
  WebRTC does not include the concept of a user identifier
Screennames, usernames, address book names, click to talk, etc. more likely
No need to work on TN replacement
  It will “just happen”
  There will be TNs and other identifiers, like today